## Slide 1: DSP: Systems
Irwan Prasetya Gunawan
Informatics Engineering
irwan.gunawan@bakrie.ac.id
Last Updated: 4/20/21

## Slide 2: Discrete-Time Systems
Discrete-Time System is a mathematical operation that maps a given input sequence x[n] into an output sequence y[n]
Example Discrete-Time Systems
  Moving (Running) Average
  Maximum
  Ideal Delay System
T{.}
x[n]
y[n]

## Slide 3: Memoryless System
Memoryless System
  A system is memoryless if the output y[n] at every value of n depends only on the input x[n] at the same value of n
Example Memoryless Systems
  Square
  Sign
Counter Example
  Ideal Delay System

## Slide 4: Linear Systems
Linear System: A system is linear if and only if
Examples
  Ideal Delay System

## Slide 5: Time-Invariant Systems
Time-Invariant (shift-invariant) Systems
  A time shift at the input causes corresponding time-shift at output
Example
  Square
Counter Example
  Compressor System

## Slide 6: Causal System
Causality
  A system is causal it’s output is a function of only the current and previous samples
Examples
  Backward Difference
Counter Example
  Forward Difference

## Slide 7: Stable System
Stability (in the sense of bounded-input bounded-output BIBO)
  A system is stable if and only if every bounded input produces a bounded output
Example
  Square
Counter Example
  Log

## Slide 8: Linear-Time Invariant System
Special importance for their mathematical tractability
Most signal processing applications involve LTI systems
LTI system can be completely characterized by their impulse response
Represent any input
From time invariance we arrive at convolution
A system that is both linear and time invariant is called a filter
T{.}
[n-k]
hk[n]

## Slide 9: LTI System Example
-5
0
5
0
1
2
-5
0
5
0
1
2
-5
0
5
0
1
2
-5
0
5
0
1
2
-5
0
5
0
1
2
-5
0
5
0
2
4
-5
0
5
0
0.5
1
-5
0
5
0
0.5
1
LTI
LTI
LTI
LTI

## Slide 10: Convolution
Note that the indexes of a and x go in opposite directions
Such that the sum of the indexes equals the output index
x0
x1
x2
x3
x4
x5
a2
a1
a0
*
*
y0
*
a2
a1
*
a0
*
*
y0
*
*
y1
*
a2
*
a1
*
*
y0
a0
*
*
*
y1
*
*
y2
*
The simplest filter types are amplification and delay
The next simplest is the moving average
a2
*
a1
*
*
y2
a0
*
*
*
y3
*
*
y4
*
y0
y1
a2
*
a1
*
*
y1
a0
*
*
*
y2
*
*
y3
*
y0
a2
*
a1
*
*
y3
a0
*
*
*
y4
*
*
y5
*
y0
y1
y2

## Slide 11: Convolution
You know all about convolution !
LONG MULTIPLICATION B3 B2 B1 B0
* A3 A2 A1 A0
-----------------------------------------------
A0B3 A0B2 A0B1 A0B0
A1B3 A1B2 A1B1 A1B0
A2B3 A2B2 A2B1 A2B0
A3B3 A3B2 A3B1 A3B0
------------------------------------------------------------------------------------
POLYNOMIAL MULTIPLICATION
(a3 x3 +a2 x2 + a1 x + a0) (b3 x3 +b2 x2 + b1 x + b0) =
a3 b3 x6 + … + (a3 b0 + a2 b1 + a1 b2 + a0 b3 ) x3 + … + a0 b0

## Slide 12: Array algorithm

## Slide 13: Properties of LTI Systems
Convolution is commutative
Convolution is distributive
h[n]
x[n]
y[n]
x[n]
h[n]
y[n]
h1[n]
x[n]
y[n]
h2[n]
+
h1[n]+ h2[n]
x[n]
y[n]

## Slide 14: Properties of LTI Systems
Cascade connection of LTI systems
h1[n]
x[n]
h2[n]
y[n]
h2[n]
x[n]
h1[n]
y[n]
h1[n]h2[n]
x[n]
y[n]

## Slide 15: Stable and Causal LTI Systems
An LTI system is (BIBO) stable if and only if
  Impulse response is absolute summable
  Let’s write the output of the system as
  If the input is bounded
  Then the output is bounded by
  The output is bounded if the absolute sum is finite
An LTI system is causal if and only if

## Slide 16: Linear Constant-Coefficient Difference Equations (LCCDE)
An important class of LTI systems of the form
The output is not uniquely specified for a given input
  The initial conditions are required
  Linearity, time invariance, and causality depend on the initial conditions
  If initial conditions are assumed to be zero system is linear, time invariant, and causal
Example
  Moving Average
  Difference Equation Representation

## Slide 17: Eigenfunctions of LTI Systems
Complex exponentials are eigenfunctions of LTI systems:
Let’s see what happens if we feed x[n] into an LTI system:
The eigenvalue is called the frequency response of the system
H(ej) is a complex function of frequency
  Specifies amplitude and phase change of the input
eigenfunction
eigenvalue

## Slide 18: Block Diagram Representation
LTI systems with rational system function can be represented as constant-coefficient difference equation
The implementation of difference equations requires delayed values of the
  input
  output
  intermediate results
The requirement of delayed elements implies need for storage
We also need means of
  addition
  multiplication

## Slide 19: Basic blocks
yn = a0 xn + a1 xn-1
yn = xn - xn-1
Explicitly draw point only when need to store value (memory point)

## Slide 20: Basic MA blocks
yn = a0 xn + a1 xn-1

## Slide 21: Example
Block diagram representation of

## Slide 22: General MA
we would like to build
but we only have 2-input adders !
tapped delay line = FIFO

## Slide 23: General MA (cont.)
Instead we can build
We still have tapped delay line = FIFO (data structure)
But now iteratively use basic block D (algorithm)
MACs

## Slide 24: General MA (cont.)
There are other ways to implement the same MA
still have same FIFO (data structure)
  but now basic block is A (algorithm)
Computation is performed in reverse
There are yet other ways (based on other blocks)
FIFO
MACs

## Slide 25: Basic AR block
One way to implement
Note the feedback
Whenever there is a loop, there is recursion (AR)
There are 4 basic blocks here too

## Slide 26: General AR filters
There are many ways to implement the general AR
Note the FIFO on outputs
  and iteration on basic blocks

## Slide 27: ARMA filters
The straightforward implementation :
Note L+M memory points
Now we can demonstrate
  how to use graph theory
  to save memory

## Slide 28: ARMA filters (cont.)
We can commute
  the MA and AR filters
  (any 2 filters commute)
Now that there are points representing
  the same signal !
Assume that L=M (w.o.l.g.)

## Slide 29: ARMA filters (cont.)
So we can use only one point
And eliminate redundant branches

## Slide 30: Allowed transformations
Geometrical transformations that do no change topology
Commutation of any two filters
Unification of identical points (signals)
and elimination of un-needed branches
Transposition theorem
  exchange input and output
  reverse all arrows
  replace adders with splitters
  replace splitters with adders

## Slide 31: A peek at the z-Transform
Generalization of the Fourier Transform
  Fourier Transform does not exist for all signals
The z-Transform is often time more convenient to use
Definition:
Compare to DTFT definition:
z is a complex variable that can be represented as z=r ej
Substituting z=ej will reduce the z-transform to DTFT
Will discuss more on z-Transform in later chapters

## Slide 32: Z-Transform Properties: Linearity
Notation
Linearity
Time Shifting
Convolution

## Slide 33: Direct Form I
General form of difference equation
Alternative equivalent form

## Slide 34: Direct Form I
Transfer function can be written as
Direct Form I Represents

## Slide 35: Alternative Representation
Replace order of cascade LTI systems

## Slide 36: Alternative Block Diagram
We can change the order of the cascade systems

## Slide 37: Direct Form II
No need to store the same data twice in previous system
So we can collapse the delay elements into one chain
This is called Direct Form II or the Canonical Form
Theoretically no difference between Direct Form I and II
Implementation wise
  Less memory in Direct II
  Difference when using finite-precision arithmetic

## Slide 38: Graph theory
x
y
y = x
x
y
a
y = a x
x
z
y
y = x
and
z = x
x
z
y
z = x + y
z = x - y
x
z
y
-
y = z-1 x
x
y
z-1
DSP graphs are made up of
points
directed lines
special symbols
points = signals
all the rest = signal processing systems
splitter = tee connector
unit delay
adder
identity = assignment
gain

## Slide 39: Why is graph theory useful ?
DSP graphs capture both
algorithms and
data structures
Their meaning is purely topological
Graphical mechanisms for simplifying (lowering MIPS or memory)
Four basic transformations
Topological (move points around)
Commutation of filters (any two filters commute!)
Identification of identical signals (points) and removal of redundant branches
Transposition theorem

## Slide 40: Signal Flow Graph Representation
Similar to block diagram representation
  Notational differences
A network of directed branches connected at nodes
Example representation of a difference equation

## Slide 41: Example
Representation of Direct Form II with signal flow graphs

## Slide 42: Determination of System Function from Flow Graph

## Slide 43: Basic Structures for IIR Systems: Direct Form I

## Slide 44: Basic Structures for IIR Systems: Direct Form II

## Slide 45: Filters
Filters have an important property
Y() = H() X() Yk = Hk Xk
In particular, if the input has no energy at frequency f
  then the output also has no energy at frequency f
  (what you get out of it depends on what you put into it)
This is the reason to call it a filter
  just like a colored light filter (or a coffee filter …)
Filters are used for many purposes, for example
filtering out noise or narrowband interference
separating two signals
integrating and differentiating
emphasizing or de-emphasizing frequency ranges

## Slide 46: Filter design
low pass
f
high pass
f
band pass
f
band stop
f
notch
f
multiband
f
realizable LP
When designing filters, we specify
transition frequencies
transition widths
ripple in pass and stop bands
linear phase (yes/no/approximate)
computational complexity
memory restrictions