## Slide 1: Discrete Fourier Transform
Digital Signal Processing
Irwan Prasetya Gunawan
Informatics Engineering
irwan.gunawan@bakrie.ac.id
Last Updated: 6/15/21

## Slide 2: Fourier analysis - applications
Applications wide ranging and ever present in modern life
  Telecomms - GSM/cellular phones,
  Electronics/IT - most DSP-based applications,
  Entertainment - music, audio, multimedia,
  Accelerator control (tune measurement for beam steering/control),
  Imaging, image processing,
  Industry/research - X-ray spectrometry, chemical analysis (FT spectrometry), PDE solution, radar design,
  Medical - (PET scanner, CAT scans & MRI interpretation for sleep disorder & heart malfunction diagnosis,
  Speech analysis (voice activated “devices”, biometry, …).

## Slide 3: Summary: Fourier analysis - tools
Input Time Signal Frequency spectrum
Discrete
Discrete
DFS
Periodic (period T)
Continuous
DTFT
Aperiodic
Discrete
DFT
**
**
Calculated via FFT
**
Periodic (period T)
Discrete
Continuous
FT
Aperiodic
FS
Continuous
Note: j =-1,  = 2/T, s[n]=s(tn), N = No. of samples

## Slide 4
=
3 sin(x)
A
+ 1 sin(3x)
B
A+B
+ 0.8 sin(5x)
C
A+B+C
+ 0.4 sin(7x)
D
A+B+C+D
Reminder: sum of sines and cosines
sin(x)
A
Notes: Accept without proof that every function is a sum of
sines/cosines
As frequency increases – more details are added
Low frequency – main details
Hight frequency – fine details
Coef decreases with the frequency

## Slide 5: Reminder: CT Fourier Transform
CT Fourier transform maps a time domain frequency signal to the frequency domain via
The Fourier transform is used to
  Analyse the frequency content of a signal
  Design a system/filter with particular properties
  Solve differential equations in the frequency domain using algebraic operators
Note that the transform/integral is not defined for some signals (infinite energy)

## Slide 6: Derivation of the DT Fourier Transform
By analogy with the CT Fourier transform, we might “guess”
This is because tn, & the integral operator represents the limit of a sum as the sum’s width tends to zero.
X(ejw) is periodic of period 2p, so is ejwn. Try substituting into the inverse Fourier transform with integral over 2p:
which is the original DT signal.

## Slide 7: Discrete Time Fourier Transform (DTFT)
The DT Fourier transform analysis and synthesis equations are therefore:
The function X(ejw) is referred to as the discrete-time Fourier transform and the pair of equations are referred to as the Fourier transform pair
X(ejw) is sometimes referred to as the spectrum of x[n] because it provides us with information on how x[n] is composed of complex exponentials at different frequencies
It converges when the signal is absolutely summable

## Slide 8: Example 1: 1st Order System, Decay Power
Calculate the DT Fourier transform of the signal:
Therefore:
a=0.8
stable system

## Slide 9: Example 2: Rectangular Pulse
Consider the rectangular pulse
and the Fourier transform is
N1=2

## Slide 10: Example 3: Impulse Signal
Fourier transform of the DT impulse signal is

## Slide 11: DTFT Properties: Periodicity, Linearity & Time
The DT Fourier transform is always periodic with period 2p, because
X(ej(w+2p)) = X(ejw)
It is relatively straightforward to prove that the DT Fourier transform is linear, i.e.
Similarly, if a DT signal is shifted by n0 units of time

## Slide 12: Summary of Fourier Transforms (so far…)
 | Time |  | Frequency | 
Fourier Series (FS) | Continuous Periodic |  | Discrete Infinite | 
Fourier Transform (FT / CTFT) | Continuous Infinite |  | Continuous Infinite | 
Discrete-Time Fourier Transform (DTFT) | Discrete Infinite |  | Continuous Periodic | 
 | Time |  | Frequency | 
Fourier Series (FS) | Continuous Periodic |  | Discrete Infinite | 
Fourier Transform (FT / CTFT) | Continuous Infinite |  | Continuous Infinite | 
Discrete-Time Fourier Transform (DTFT) | Discrete Infinite |  | Continuous Periodic | 
Frequency: Discrete Finite
Time: Discrete Finite
?

## Slide 13: Discrete FT
Discrete finite/periodic x[n]
Discrete finite/periodic X[k]
A finite/periodic sequence has only N unique values, for
Spectrum is completely defined by N distinct frequency samples
Divide into N equal steps
N

## Slide 14
Discrete Functions through sampling
0 1 2 3 ... N-1
f(x)
f(x0)
f(x0+Dx)
f(x0+2Dx)
f(x0+3Dx)
f(n) = f(x0 + nDx)
x0
x0+Dx
x0+2Dx
x0+3Dx
The discrete function f:
{ f(0), f(1), f(2), … , f(N-1) }

## Slide 15: Sampling the Fourier Transform
Consider an aperiodic sequence with a Fourier transform
Assume that a sequence is obtained by sampling the DTFT
Since the DTFT is periodic resulting sequence is also periodic
The sampling points are shown in figure
could be the DFS of a sequence
Write the corresponding sequence

## Slide 16: Sampling the Fourier Transform Cont’d
The only assumption made on the sequence is that DTFT exist
Combine equation to get
Term in the parenthesis is
So we get

## Slide 17: Sampling the Fourier Transform Cont’d
Samples of the DTFT of an aperiodic sequence
  can be thought of as DFS coefficients
  of a periodic sequence
  obtained through summing periodic replicas of original sequence
If the original sequence
  is of finite length
  and we take sufficient number of samples of its DTFT
  the original sequence can be recovered by
It is not necessary to know the DTFT at all frequencies
  To recover the discrete-time sequence in time domain
Discrete Fourier Transform
  Representing a finite length sequence by samples of DTFT

## Slide 18: DFT and IDFT
Consider an N-sequence xn (at most N non-zero values for 0  n  N-1)
uniformly spaced frequency samples
(4.21.1)
(4.21.2)
DFT:
Finite sum! Therefore, it’s computable.
(4.21.1) can be rewritten as:
(4.21.3)
(4.21.4)
(4.21.5)
Btw, DFT is a sampled version of DTFT.

## Slide 19: DFT and IDFT (cont)
Let us verify (4.21.5). We multiply both sides by
(4.22.1)
(4.22.2)
(4.22.3)
(4.22.4)

## Slide 20: The Discrete Fourier Transform
Consider a finite length sequence x[n] of length N
For given length-N sequence associate a periodic sequence
The DFS coefficients of the periodic sequence are samples of the DTFT of x[n]
Since x[n] is of length N there is no overlap between terms of x[n-rN] and we can write the periodic sequence as
To maintain duality between time and frequency
  We choose one period of as the Fourier transform of x[n]

## Slide 21: The Discrete Fourier Transform Cont’d
The DFS pair
The equations involve only on period so we can write
The Discrete Fourier Transform
The DFT pair can also be written as

## Slide 22: Properties of DFT
Linearity
Duality
Circular Shift of a Sequence

## Slide 23: Example: Duality

## Slide 24: Relation between DTFT and DFT
1. Sampling of DTFT
(4.24.1)
(4.24.2)
(4.24.3)
yn is an infinite sum of shifted replicas of xn. Iff xn is a length M sequence (M  N) than yn = xn. Otherwise, time-domain aliasing  xn cannot be recovered!

## Slide 25: Relation between DTFT and DFT (cont)
2. DTFT from DFT by Interpolation
Let xn be a length N sequence:
It’s possible to determine DTFT X(ej) from its uniformly sampled version uniquely!
Let us try to recover DTFT from DFT (its sampled version).
(4.25.1)
(4.25.2)
(4.25.3)

## Slide 26: Relation between DTFT and DFT (cont 2)
3. Numerical computation of DTFT from DFT
Let xn is a length N sequence:
defined by N uniformly spaced samples
We wish to evaluate at more dense frequency scale.
No change in information, no change in DTFT… just a better “plot resolution”.
(4.26.1)
Define:
zero-padding
(4.26.2)
(4.26.3)

## Slide 27: Discrete Fourier Transform
The DFT pair was given as
Baseline for computational complexity:
  Each DFT coefficient requires
    N complex multiplications
    N-1 complex additions
  All N DFT coefficients require
    N2 complex multiplications
    N(N-1) complex additions
Complexity in terms of real operations
    4N2 real multiplications
    2N(N-1) real additions
Most fast methods are based on symmetry properties
  Conjugate symmetry
  Periodicity in n and k

## Slide 28: FFT
In the matrix form:
where:
(4.23.1)
(4.23.2)
(4.23.3)
(4.23.4)
(4.23.5)
(4.23.6)
(4.23.7)
This is actually FFT…

## Slide 29: Decimation-In-Time FFT Algorithms
Makes use of both symmetry and periodicity
Consider special case of N an integer power of 2
Separate x[n] into two sequence of length N/2
  Even indexed samples in the first sequence
  Odd indexed samples in the other sequence
Substitute variables n=2r for n even and n=2r+1 for odd
G[k] and H[k] are the N/2-point DFT’s of each subsequence

## Slide 30: Decimation In Time
8-point DFT example using decimation-in-time
Two N/2-point DFTs
  2(N/2)2 complex multiplications
  2(N/2)2 complex additions
Combining the DFT outputs
  N complex multiplications
  N complex additions
Total complexity
  N2/2+N complex multiplications
  N2/2+N complex additions
  More efficient than direct DFT
Repeat same process
  Divide N/2-point DFTs into
  Two N/4-point DFTs
  Combine outputs

## Slide 31: Decimation In Time Cont’d
After two steps of decimation in time
Repeat until we’re left with two-point DFT’s

## Slide 32: Decimation-In-Time FFT Algorithm
Final flow graph for 8-point decimation in time
Complexity:
  Nlog2N complex multiplications and additions

## Slide 33: Butterfly Computation
Flow graph constitutes of butterflies
We can implement each butterfly with one multiplication
Final complexity for decimation-in-time FFT
  (N/2)log2N complex multiplications and additions

## Slide 34: In-Place Computation
Decimation-in-time flow graphs require two sets of registers
  Input and output for each stage
Note the arrangement of the input indices
  Bit reversed indexing

## Slide 35: Decimation-In-Frequency FFT Algorithm
The DFT equation
Split the DFT equation into even and odd frequency indexes
Substitute variables to get
Similarly for odd-numbered frequencies

## Slide 36: Decimation-In-Frequency FFT Algorithm
Final flow graph for 8-point decimation in frequency

## Slide 37: Famous Fourier Transforms
Sine wave
Delta function

## Slide 38: Famous Fourier Transforms
Gaussian
Gaussian

## Slide 39: Famous Fourier Transforms
Sinc function
Square wave

## Slide 40: Famous Fourier Transforms
Sinc function
Square wave

## Slide 41: Famous Fourier Transforms
Exponential
Lorentzian

## Slide 42: FFT of FID

## Slide 43: FFT of FID

## Slide 44: FFT of FID

## Slide 45: Examples….

## Slide 46: Spectrum (computed through FFT)
Peak
energies

## Slide 47: Spectrum (computed through FFT)

## Slide 48: Spectrum (computed through FFT)
Raw
Filtered

## Slide 49: Spectrum (computed through FFT)
Simulated
Noise using
Tones at
185 Hz,
246 Hz,
308 Hz,
370 Hz

## Slide 50
(u = 0,..., N-1)
(x = 0,..., N-1)
1D Discrete Fourier Transform:
The Discrete Fourier Transform
2D Discrete Fourier Transform:
(x = 0,..., N-1; y = 0,…,M-1)
(u = 0,..., N-1; v = 0,…,M-1)

## Slide 51
Fourier spectrum log(1 + |F(u,v)|)
Image f
The Fourier Image
Fourier spectrum |F(u,v)|

## Slide 52
Image f
The Fourier Image
Fourier spectrum |F(u,v)|

## Slide 53
Frequency Bands
Percentage of image power enclosed in circles (small to large) :
90%, 95%, 98%, 99%, 99.5%, 99.9%
Image
Fourier Spectrum

## Slide 54
Low pass Filtering
90%
95%
98%
99%
99.5%
99.9%

## Slide 55
2D Image
2D Image - Rotated
Fourier Spectrum
Fourier Spectrum
Rotation

## Slide 56
Image
Domain
Frequency
Domain
Fourier Transform -- Examples

## Slide 57
Image
Fourier spectrum
Fourier Transform -- Examples

## Slide 58
Noise Removal
Noisy image
Fourier Spectrum
Noise-cleaned image

## Slide 59
High Pass Filtering
Original
High Pass Filtered

## Slide 60
High Frequency Emphasis
+
Original
High Pass Filtered

## Slide 61
High Frequency Emphasis
Original
High Frequency Emphasis
Original
High Frequency
Emphasis

## Slide 62
Original
High pass Filter
High Frequency
Emphasis
High Frequency Emphasis
+
Histogram Equalization
High Frequency Emphasis

## Slide 63: Compare – JPEG encoded image
Teach a machine/computer to recognize the original image to be able to rate the quality of the degraded one.
Tell the machine/computer to identify any differences between the images.

## Slide 64: Feature Extraction Models
Division of horizontal (H) and vertical (V) spatial activity into HV (shaded) and Non-HV (white) distributions (Wolf and Pinson, 1999).

## Slide 65: Harmonic analysis: review
Luminance discontinuities in coded picture act as pseudo-periodic pattern in spatial domain, and will generate harmonics in frequency domain
Actual 32  32 gradient image
A
B
Luminance level of pixels along AB
Pseudo-periodic pattern
Fourier Transform
Harmonics
Fundamental
Ref: Irwan Prasetya Gunawan andMohammed Ghanbari (2008). “Reduced-Reference Video Quality Assessment using Discriminative Local Harmonic Strength with Motion Consideration”, IEEE Transaction on Circuits and Systems for Video Technology, Vol. 18, No. 1, January 2008, pp. 71–83.
Notes: Detection of blockiness

## Slide 66: Examples
Identifying blocky picture using harmonic gain:
Ref: Irwan Prasetya Gunawan and Mohammed Ghanbari (2005).“Image Quality Assessment Based On Harmonics Gain/Loss Information”, in Proc. ICIP’05, IEEE International Conference on Image Processing 2005 (Genoa, Italy), Volume: 1, pp. 429 – 432, 11-14 Sept. 2005.

## Slide 67: Summary: Fourier analysis - tools
Input Time Signal Frequency spectrum
Discrete
Discrete
DFS
Periodic (period T)
Continuous
DTFT
Aperiodic
Discrete
DFT
**
**
Calculated via FFT
**
Periodic (period T)
Discrete
Continuous
FT
Aperiodic
FS
Continuous
Note: j =-1,  = 2/T, s[n]=s(tn), N = No. of samples