## Slide 1
Untuk yang sudah bergabung:
Tuliskan nama dan NIM di bagian chat (klik di bagian kiri bawah layar)
Ajak teman lainnya yang mungkin belum bergabung di sini untuk mengikuti kelas
Bantu temannya dengan mengapprove teman yang akan join class meeting
Cam on untuk dokumentasi dan syarat presensi kelas
Screenshot sample pada saat kelas mulai, termasuk absensi manual dengan nama/NIM masing-masing, screenshot video meeting dengan cam on dan off dengan tampilan materi perkuliahan saat ini
Upload screenshot sample ke web E-Learning di alamat weekly meeting yang sudah ditentukan
Absensi melalui pemanggilan nama masing-masing akan dilakukan di 30 menit awal perkuliahan
Ketika kuliah berlangsung:
Mute Sound
Jika akan bertanya (atau ditanya), unmute sound
Unmute sound di laptop/PC bisa dilakukan dengan menekan Space Bar
Selasa, 23 Maret 2021 – start 07.45 WIB

## Slide 2: Operations on Signal
Digital Signal Processing
Irwan Prasetya Gunawan
Informatics
irwan.gunawan@bakrie.ac.id
Last Updated: 3/30/21

## Slide 3: Brief review: DSP
Why DSP ? use (digital) computer instead of (analog) electronics
more flexible
  new functionality requires code changes, not component changes
more accurate
  even simple amplification can not be done exactly in electronics
more stable
  code performs consistently
more sophisticated
  can perform more complex algorithms
However
digital computers only process sequences of numbers
  not analog signals
requires converting analog signals to digital domain for processing
and digital signals back to analog domain

## Slide 4: Signals
Speech sounds can be described as acoustic pressure that changes with time

## Slide 5: Signals (cont’d)
In addition to one-dimensional signal, we will often find two-dimensional signals. An example is the digital image. Consider a monochromatic image. Monochromatic image represented by the level of brightness as a function of the coordinates.

## Slide 6: Signal representations
Analog signal
s(t)
continuous time
- < t < +
Digital signal
sn
discrete time
n = - … +
Physicality requirements
s values are real
s values defined for all times
Finite energy
Finite bandwidth
Mathematical usage
s may be complex
s may be singular
Infinite energy allowed
Infinite bandwidth allowed
Energy = how "big" the signal is
Bandwidth = how "fast" the signal is

## Slide 7: Signal representations (examples)
Continuous-time signals:
  x(t) = 10 sin 2t
  x(t) = 2t+7
Discrete-time signals:
  x[n]=2n+3
  y[n]=[1, 2, 3, 4, 3, 2, 1], note: the underscore ”_” is the reference point n=0.

## Slide 8: Unit Step
Discrete unit step
  u[n]=
Shifted unit step
  u[n-k]=
u[n]
-1
-2
n
1
-3
3
2
1
u[n-k]
…
-1
n
1
k
1

## Slide 9: Unit Step (cont’d)
Continuous unit step
  u(t)=
Shifted unit step
  u(t-)=
u(t- )
t

1
t
1
u(t)

## Slide 10: Unit Step (cont’d)

## Slide 11: Unit Impulse
Discrete Unit Impulse
Shifted Unit Impulse
[n]
-1
-2
n
1
-3
3
2
1
[n-k]
…
-1
n
1
k
1

## Slide 12: Unit Impulse (cont’d)
Properties of discrete unit impulse:

## Slide 13: Unit Impulse (cont’d)
Continuous Unit Impulse:
t
1/
(t)
t
0
(t)

## Slide 14: Unit Impuls (cont’d)
Shifted Unit Impulse:
Continuous Unit Impulse Properties:
t
(t-)


## Slide 15: Analog signal construction

## Slide 16: Representing signal with impulses

## Slide 17: Representing signal with impulses

## Slide 18: Representing signal with impulses

## Slide 19: Discrete (digital) signal construction

## Slide 20: Some digital “signals”
Zero signal
Constant signal
(  energy!)
Unit Impulse (UI)
Shifted Unit Impulse (SUI)
Step
(  energy!)
n=0
n=0
1
n=0
1
n=1
1
n=0

## Slide 21: Some periodic digital “signals”
Square wave
Triangle wave
Saw tooth
Sinusoid
(not always periodic!)
1
n=0
-1

## Slide 22: Signal types
Signals (analog or digital) can be:
deterministic or stochastic
if stochastic : white noise or colored noise
if deterministic : periodic or aperiodic
finite or infinite time duration

## Slide 23: Signal types

## Slide 24: Signal types
Signals are more than their representation(s)
we can invert a signal y = -x
we can time-shift a signal y = zm x
we can add two signals z = x + y
we can compare two signals (correlation)
various other operations on signals
  first finite difference y = D x means yn = xn - xn-1
    Note D = 1 - z-1
  higher order finite differences y = Dm x
  accumulator y =  x means yn = Sm=-n xm
    Note  D = D  = 1
  Hilbert transform

## Slide 25: Digital signals and vectors
Digital signals are in many ways like vectors
… s-5 s-4 s-3 s-2 s-1 s0 s1 s2 s3 s4 s5 …  (x, y, z)
In fact, they form a linear vector space
the zero vector 0 (0n = 0 for all times n)
every two signals can be added to form a new signal x + y = z
every signal can be multiplied by a real number (amplified!)
every signal has an opposite signal -s so that s + -s = 0 (zero signal)
every signal has a length - its energy
Similarly, analog signals, periodic signals with given period, etc.
However
they are (denumerably) infinite dimension vectors
the component order is not arbitrary (time flows in one direction)
  time advance operator z (z s)n = sn+1
  time delay operator z-1 (z-1 s)n = sn-1

## Slide 26: Example
Dial tone
DTMF pulse
Busy tone

## Slide 27: Example (spectrum)
DTMF pulse
Busy tone
Dial tone
Dial tone

## Slide 28: Example (spectrum)
Dial tone
Dial Tone is sent to a customer or operator to indicate that the receiving end is ready to receive dial pulses or DTMF signals.

## Slide 29
z[n]
x[n]
y[n]

## Slide 30: Analog to Digital Conversion
To convert “real-world” analog signals to digital signals for processing
Sampling
Quantizing and coding
Xa(t)
X [n]
Xq[n]
Sampler
Quantizer
and Coder
Analog signal
Discrete signal
Digital signal

## Slide 31
xa(t)
n=-¥
¥
S(t) = åd(t- nT)
x
´
xs(t) = å xa(nT) d(t- nT)
n=-¥
¥
convert to
discrete
sequence
x[n] = xa(nT)

## Slide 32: Sampling
From an analog signal we can create a digital signal
  by SAMPLING
Under certain conditions
  we can uniquely return to the analog signal
Nyquist (Low pass) Sampling Theorem
if the analog signal is BW limited and
  has no frequencies in its spectrum above FNyquist
then sampling at above 2FNyquist causes no information loss

## Slide 42: Sampling
Uniform
  One sample every T seconds (ideally)
  x[n] = xa(nT), -¥<n<+¥
  Sampling period: T
  Sampling frequency: Fs=1/T
Assume: xa(t) = Acos( 2pFt+q) = Acos(W t+q)
Then: x[n] = Acos[2pFnT+q] = Acos[W Tn+q]
= Acos[w n+q], where w =W T is called the normalized or discrete domain frequency

## Slide 43
f = F/Fs must be rational in order for x[n] to be periodic
If f = k/N, then x[n] is periodic with period N
Now, xa(nT) = Acos(W Tn+q)
= Acos((W +2pk/T)Tn+q)
is periodic in W with period 2p/T
Also, x[n] = Acos[w n+q] = Acos[(w+2pk) n +q] is periodic in w with period 2p

## Slide 44: Example
Consider the analog signal:
  xa(t) = 3cos( 2000pt) +5sin( 6000pt) +
  10cos( 12000pt)
What is the Nyquist rate for this signal?
The max. frequency in xa(t) is fMAX=6 Khz
The Nyquist rate is 12 Khz

## Slide 45
xa(t) = 3cos( 2000pt)+5sin( 6000pt)+10cos(12000pt)
If the signal is sampled at FS = 5000 samples/sec, what is the discrete time signal obtained after sampling?
x[n] = xa(nT) = xa(n/5000)
= 3cos(2pn/5)+5sin(6pn/5)+10cos(12pn/5)
= 13cos(2pn/5)+5sin(2pn3/5)
= 13cos(2pn/5)-5sin(2pn2/5)

## Slide 46
xa(t) = 3cos( 2000pt)+5sin( 6000pt)+10cos(12000pt)
What is the analog signal that can be reconstructed from the resulting discrete signal, assuming ideal interpolation?
3/2
3/2
5
5/2j
5
-5/2j
5
3/2
3/2
5/2j
3/2
-5/2j
3/2
5
-5/2j
3/2
13/2
13/2
5/2j
13/2
-5/2j
3/2
13/2
5/2j
13/2
13/2
5/2j
-5/2j

## Slide 47
xa(t) = 13cos( 2000pt)-5sin( 4000pt)
^
Resulting analog signal after perfect interpolation:

## Slide 48: Reconstruction
Frequency response of ideal reconstruction filter
-Wc
Wc
T
Impulse response of ideal reconstruction filter
Hr(jW) = {
T, Wc<W£Wc
0, otherwise
hr(t)=
sin pt/T
pt/T

## Slide 49
xa(t)
xs(t)
hr(t)
xr(t)

## Slide 50: Quantization and coding
Quantization:
  Converting discrete time signal to digital
  xq(n) =Q [x(n)]
D
Quantization
step

## Slide 51
x
Q(x)
D
D/2
7D/2
5D/2
-D/2
-5D/2
-3D/2
-7D/2
3D/2
2D
3D
-D
-2D
-3D
-4D

## Slide 52: Quantization
Rounding: Assign x[n] to the closest quantization level
Quantization error
  eq[n] = xq[n] - x[n]
  -D/2 £ eq[n] £ D/2
  Uniformly distributed
    mean = 0
    variance = D2/12

## Slide 53: Quantization
Range of quantizer: xmax-xmin
Quantization levels: m
Assuming uniform quantization
  =
  = 2Xm/ (m-1)
  where Xm = (xmax-xmin)/2 is called the full-scale level of the A/D converter
m-1
xmax-xmin

## Slide 54: Coding
Coding is the process of assigning a unique binary number to each quantization level
Number of bits required ³ log2m
Alternatively, given b+1 bits
D = (xmax-xmin)/2b+1 =Xm /2b
For A/D devices, the higher Fs and m, the less the error (and the more the cost of the device)

## Slide 55: Assignment
Ch. 2 Assignment:
  2.1.2
  2.2.4
  2.2.5 (use Matlab/Octave)
  2.2.7 (for asymmetric unit impulse only)
  2.3.3
  2.4.3
  2.5.3
  2.6.1
  2.6.3
Submission:
  Time/date due: Monday, 16 March 2020, 23:55 PM
  Submission procedure: upload via E-learning
  Typed answers, submit in a pdf file
  For Matlab/Octave, upload the m files but include any figures/graph in the submitted pdf file
  Filename format: DSP_A02_name_studentnumber.[pdf]

## Slide 56: Important Notes
Please note that this is an individual assignment and therefore no two students should write the same answers!
Cheating, plagiarism, copy-paste other people's work (incl. your friend's work) without giving appropriate credits will incur discount on your grades
Don't just answer by pointing out your references in your assignment without giving any further, necessary explanations (for example, you might be tempted to write: "Answer for Number 1 can be found in http://www.dspguide.com"); write your answer in your own words by making use of the references
In citing your references, you can any citation methods/style you'd might like; e.g.
  Numerical style such as found in IEEE papers
  Author-date style
  Turabian style
  MLA style
  APA style
In MS Word (2007/2010), you'd probably like to try the citation & bibliography tools ('References >> Citation & Bibliography') to manage your reference list. Alternatively, you can also use EndNote for the same purpose (note however not all MS Word has EndNote pre-installed in its configuration). The only downside of EndNote is that it is not free.
If you're using LaTeX for writing your documents, BibTeX is very recommended. Both LaTeX and BibTeX are entirely free. You can use any general text editors you like for preparing documents in LaTeX (vi, emacs, notepad++) or alternatively use the ones more specifically designed for LaTeX preparation (e.g., TexWorks that comes with MikTeX -- a LaTeX installation for Windows, Texmaker, Lyx, etc)
Useful resources:
  Numerical and author-date style widely used in computer science engineering students: http://www.lib.monash.edu.au/tutorials/citing/compsci.html
  APA style citation method: http://www.uis.edu/ctl/writing/documents/APACitationMethods.pdf
  MLA style citation method: http://www.uis.edu/ctl/writing/MLACitation_000.pdf.pdf
  Turabian method: http://library.concordia.ca/help/howto/turabian.pdf